## Slide 1: Multipath Traffic Engineering for Segment Routing
draft-stone-spring-mpte-sr
IETF 124 – Montreal
Andrew Stone (andrew.stone@nokia.com) – Presenter
Vishnu Pavan Beeram – (vbeeram@juniper.net)
Nick Buraglio - (buraglio@forwardingplane.net)
Shaofu Peng - (peng.shaofu@zte.com.cn)

## Slide 2: -01 changes
New co-authors
Construct differentiation (Ingress vs Junction Segment)
Color mapping
DAG reusability
Path protection clarifications
Local and Global optimization
  Guidelines
  Procedures
  Examples

## Slide 3: Recap - draft-stone-spring-mpte-sr
How to achieve MPTE (draft-kompella-teas-mpte) with SR and a controller
  ECMP + Non-ECMP Slack + TE
Junction Segments deployed throughout DAG
  Incoming SID (Binding SID)
  Outgoing SID list(s)
    SR Path to Junction + Junction SID
    Weight
Junction segments realized with an SR Policy Candidate Path
B
C
A
D
G
E
F
H
Controller/PCE
PCEP/BGP/Netconf

## Slide 4
B
C
A
E
F
H
Junction Segment C
Headend: C, Color: 100, Endpoint: null
Binding SID = 101
SID List:
[ADJ-5100, 100], 0.4
[ADJ-5103, ADJ-5504], 0.6
5100
5103
5504
5002
5001
Junction Segment B
Headend: B, Color: 100, Endpoint: null
Binding SID = 100
SID List:
[NodeSID-H], 1.0
SR Policy (ingress)
Headend: A, Color: 50 Endpoint: H
SID List:
[ADJ-5002, 100], 0.5
[ADJ-5001, 101], 0.5
SR-MPLS Example

## Slide 5
B
C
A
E
F
H
Global optimization
Example newly computed DAG

## Slide 6
B
C
A
E
F
H
Junction Segment C
Headend: C, Color: 100, Endpoint: null
Binding SID = 101
SID List:
[ADJ-5100, 100], 0.4
[ADJ-5103, ADJ-5504], 0.6
5103
5504
5002
5001
Junction Segment B
Headend: B, Color: 100, Endpoint: null
Binding SID = 100
SID List:
[NodeSID-H], 1.0
SR Policy (ingress)
Headend: A, Color: 50 Endpoint: H
SID List:
[ADJ-5002, 100], 0.5
[ADJ-5001, 101], 0.5
Global optimization
1. Deploy new Junction Segments (SR Policies)
5003
Junction Segment B
Headend: B, Color: 200, Endpoint: null
Binding SID = 101
SID List:
[NodeSID-H], 0.5
[ADJ-5003, 102], 0.5
Junction Segment C
Headend: C, Color: 200, Endpoint: null
Binding SID = 102
SID List:
[ADJ-5103, ADJ-5504], 1.0
C deployed before B

## Slide 7
B
C
A
E
F
H
Junction Segment C
Headend: C, Color: 100, Endpoint: null
Binding SID = 101
SID List:
[ADJ-5100, 100], 0.4
[ADJ-5103, ADJ-5504], 0.6
5103
5504
5002
5001
Junction Segment B
Headend: B, Color: 100, Endpoint: null
Binding SID = 100
SID List:
[NodeSID-H], 1.0
SR Policy (ingress)
Headend: A, Color: 50 Endpoint: H
SID List:
[ADJ-5002, 101], 0.5
[ADJ-5001, 102], 0.5
Global optimization
2. Update ingress with new SID list (local MBB)
5003
Junction Segment B
Headend: B, Color: 200, Endpoint: null
Binding SID = 101
SID List:
[NodeSID-H], 0.5
[ADJ-5003, 102], 0.5
Junction Segment C
Headend: B, Color: 200, Endpoint: null
Binding SID = 102
SID List:
[ADJ-5103, ADJ-5504], 1.0

## Slide 8
B
C
A
E
F
H
5103
5504
5002
5001
SR Policy (ingress)
Headend: A, Color: 50 Endpoint: H
SID List:
[ADJ-5002, 101], 0.5
[ADJ-5001, 102], 0.5
Global optimization
3. Delete unused junction segments
5003
Junction Segment B
Headend: B, Color: 101, Endpoint: null
Binding SID = 101
SID List:
[NodeSID-H], 0.5
[ADJ-5003, 102], 0.5
Junction Segment C
Headend: B, Color: 101, Endpoint: null
Binding SID = 102
SID List:
[ADJ-5103, ADJ-5504], 1.0

## Slide 9: Next steps
Open to discussions and feedback
Stay aligned with concepts and feed comments back into:
  TEAS WG: draft-kompella-teas-mpte
  PCE WG: draft-beeram-pce-pcep-mpted
Work on content for manageability considerations
Co-author discussions on information model for MPTE and information signalling