## Slide 1: Multipath Traffic Engineering for Segment Routing
draft-stone-spring-mpte-sr
IETF 123 - Madrid
Andrew Stone (andrew.stone@nokia.com) – Presenter
Vishnu Pavan Beeram – (vbeeram@juniper.net)

## Slide 2: Multipath Traffic Engineering
Introduced in draft-kompella-teas-mpte
Different transport tunnel types concept comprised of:
  Traffic engineered constraints
  ECMP paths
  Non-ECMP Paths – slack x of the shortest path
  Multi-egress nodes and multi-ingress (maybe)
  Unequal weight load balancing per hop
Transport tunnel is represented as a Directed Acyclic Graph (DAG) instead of a Path
Computed by a headend ingress or a PCE
Can be centralized or distributed solution for signaling

## Slide 3: Multipath Traffic Engineering
B
C
A
D
G
E
F
H
20
10
10
10
5
5
5
5
10
10
10
10
B
C
A
D
G
E
F
H
20
10
10
10
5
5
5
5
10
10
10
10
B
C
A
D
G
E
F
H
20
10
10
10
5
5
5
5
10
10
10
10
B
C
A
D
G
E
F
H
20
10
10
10
5
5
5
5
10
10
10
10
Shortest path
Shortest ECMP path
TE Path
Multipath TE DAG
5
Te pruned

## Slide 4: draft-stone-spring-mpte-sr
B
C
A
D
G
E
F
H
Describes a centralized solution to compute and signal MPTE DAG for SR networks
Controller/PCE to compute, PCEP/BGP/Netconf to signal
The DAG is comprised of Junction Segments deployed on Junction Nodes
  Junction node is a transit node that forwards to one or more interfaces
  Similarity to Replication Segment - but load balanced, not replicated
Junction Segment is comprised of:
  Incoming SID (Binding SID)
  Outgoing SID list(s)
    Next-Junction Segment(BSID) and SR-Path stack
    Weight
A Junction segment is realized with SR Policy with a single candidate path
Controller/PCE
PCEP/BGP/Netconf

## Slide 5: ….but just use SR Policy w/multiple segment lists
Yes !
But… depending on the topological graph and size of the DAD, this could be a significant number of paths.
+ Deviating shortest path significantly can impact MSD of the SID list
+ Ingress only load balancing vs per junction node load balancing.
Decision to use many SID lists on headend or MPTE solution would be scenario dependent

## Slide 6: Junction Segment Partial, simple example with SR-MPLS
B
C
A
E
F
H
Junction Segment C
Binding SID = 101
SID List:
[5100, 100], 0.4
[5101, 102], 0.6
5100
5101
5201
5301
5501
5002
5001
- Node SIDs are value NodeSID-{letter}
- Link values are adjacency SIDs
- SID List Pos-0 is top of stack
Junction Segment B
Binding SID = 100
SID List:
[NodeSID-H]
Junction Segment F
Binding SID = 102
SID List:
[102], 1.0
Headend-A
SID List:
[5002, 100], 0.5
[5001, 101], 0.5
Could be optimized out like E, used as an example
Takes SR shortest path to H, skips the need for junction on E

## Slide 7: Junction Segment
Junction Segment C – SR Policy
Headend: C
Endpoint: 0.0.0.0
Color: <MID+VERSION>
Binding SID = 101
SID List:
[5100, 101], 0.4
[5101, 102], 0.6
Realized by SR Policy with a single candidate path
An SR Policy is unique by {Headend, Endpoint, Color}
Multiple endpoints -> use 0.0.0.0
draft-kompella-teas-mpte describes instance of the DAG is the Multipath TED(MPTED), which is identified by the MID and has a version.
  Useful to know DAG membership of the Junction Segment (SR Policy)
  -> encode MID+Version in the color attribute (**)
    Need to make sure color range is reserved block
    ** An idea...perhaps new candidate path property

## Slide 8: Hierarchy
B
C
A
D
G
E
F
H
The ingress SR Policy of the DAG can also have a binding SID
The DAG can be re-used by multiple upstream SR Paths (could be a DAG itself too)
X
Y
Headend-A
BSID-200
Headend-X
SID-List:
[NodeSID-A, 200]
Headend-Y
SID-List:
[NodeSID-A, 200]
DAG 1000

## Slide 9: draft-stone-spring-mpte-sr Other properties
Protocol support (signal/state feedback) – most already there (TBD MID+Version!)
Junction Segment optimization - don’t need on every router - leap-frog transit node(s) with SID list
Protection - TI-LFA on each SID list as per usual
  Node protection for Junction node (the BSID) is a more complicated discussion…
Multi-egress -> yes.
Multi-ingress -> … could be managed by controller in a top-down manner
Broadcast-links -> yes
Optimization – Local/global - DAG MBB:
  Needs more considerations, procedures described and potentially protocol extensions
  Can take the learnings and procedures from SR P2MP Policy

## Slide 10: Informational or Standards track?
No new extensions defined...yet
Standards track for now – primarily informational content in document
  May need extensions for things such as signalling MID+Version
  May need extensions to deal with optimization/make before break scenarios

## Slide 11: Next steps
Open to discussions, feedback and collaboration
Stay aligned with concepts in draft-kompella-teas-mpte as it evolves
Decide on MID/Version/Color attribute – new segment type(?)
Determine procedure details for optimization/MBB