## Slide 1: Multipath Traffic Engineering for Segment Routing
draft-stone-spring-mpte-sr
IETF 126 – Vienna
TEAS WG Session
Andrew Stone (andrew.stone@nokia.com) – Presenter
Vishnu Pavan Beeram – (vishnupavan.ietf@gmail.com)
Nick Buraglio - (buraglio@forwardingplane.net)
Shaofu Peng - (peng.shaofu@zte.com.cn)
Zafar Ali – (zali.cisco.com)
Siva Sivabalan – (ssivabal@ciena.com)
Jie Dong – (jie.dong@huawei.com)

## Slide 2: draft-stone-spring-mpte-sr
How to achieve MPTE (draft-kompella-teas-mpte) with SR and a controller
  ECMP + Non-ECMP Slack + TE
Controller/PCE to compute, PCEP/BGP/Netconf to signal
Junction Segments deployed throughout DAG
  Incoming SID (Binding SID)
  Outgoing SID list(s)
    SR Path to Junction + Junction SID
    Weight
B
C
A
D
G
E
F
H
Controller/PCE
PCEP/BGP/Netconf

## Slide 3: Junction Segment
Junction Segment C – SR Policy
Headend: C
Endpoint: 0.0.0.0
Color: <MID+VERSION>
Binding SID = 101
SID List:
[5100, 101], 0.4
[5101, 102], 0.6
Realized by SR Policy with a single candidate path
An SR Policy is unique by {Headend, Endpoint, Color}
Multiple endpoints -> use 0.0.0.0
MID and version tracked by the controller

## Slide 4
B
C
A
E
F
H
Junction Segment C
Headend: C, Color: 100, Endpoint: null
Binding SID = 101
SID List:
[ADJ-5100, 100], 0.4
[ADJ-5103, ADJ-5504], 0.6
5100
5103
5504
5002
5001
Junction Segment B
Headend: B, Color: 100, Endpoint: null
Binding SID = 100
SID List:
[NodeSID-H], 1.0
SR Policy (ingress)
Headend: A, Color: 50 Endpoint: H
SID List:
[ADJ-5002, 100], 0.5
[ADJ-5001, 101], 0.5
SR-MPLS Example

## Slide 5: Hierarchy
B
C
A
D
G
E
F
H
The ingress SR Policy of the DAG can also have a binding SID
The DAG can be re-used by multiple upstream SR Paths (could be a DAG itself too)
X
Y
Headend-A
BSID-200
Headend-X
SID-List:
[NodeSID-A, 200]
Headend-Y
SID-List:
[NodeSID-A, 200]
DAG 1000

## Slide 6: Other SR specific properties
Protocol signaling support (provision/state loop) – exist in BGP/PCEP/Netconf
Junction Segment state optimization - don’t need on every hop – SID list in between two junction nodes
Protection - TI-LFA covering each SID list as usual
Multi-egress -> yes.
Multi-ingress -> … could be managed by controller in a top-down manner
Optimization – Local/global - DAG MBB
  Document describes various high level procedure steps a controller could take

## Slide 7: Liveness
General guideline: Run S-BFD on all Junction nodes, on all outgoing segment lists
Required to get full coverage: path to next junction + junction processing
B
C
A
D
G
E
F
H
B
C
A
D
G
E
F
H

## Slide 8: Monitoring
Run Ping/Trace tests originating on all Junction nodes, on all outgoing segment lists
Controller aggregates to produce a full view
Controller/PCE
B
C
A
D
G
E
F
H
38ms
35ms
34ms
37ms
42ms
A->C measures one strand
Controller computes deltas to determine min, max, estimate delay via SID List to C
44ms
43ms
Ping from A to C will be weight hashed out of C unless cycle entropy, which can cascade through multiple junctions

## Slide 9: Next steps
Open to discussions and feedback
Work is taking place in SPRING WG