## Slide 1: Multipath Traffic Engineering for Segment Routing
draft-stone-spring-mpte-sr
IETF 126 – Vienna
SPRING WG Session
Andrew Stone (andrew.stone@nokia.com) – Presenter
Vishnu Pavan Beeram – (vishnupavan.ietf@gmail.com)
Nick Buraglio - (buraglio@forwardingplane.net)
Shaofu Peng - (peng.shaofu@zte.com.cn)
Zafar Ali – (zali.cisco.com)
Siva Sivabalan – (ssivabal@ciena.com)
Jie Dong – (jie.dong@huawei.com)

## Slide 2: Recap - draft-stone-spring-mpte-sr
How to achieve MPTE (draft-kompella-teas-mpte) with SR and a controller
  ECMP + Non-ECMP Slack + TE
Junction Segments deployed throughout DAG
  Incoming SID (Binding SID)
  Outgoing SID list(s)
    SR Path to Junction + Junction SID
    Weight
Junction segments realized with an SR Policy Candidate Path
B
C
A
D
G
E
F
H
Controller/PCE
PCEP/BGP/Netconf

## Slide 3
B
C
A
E
F
H
Junction Segment C
Headend: C, Color: 100, Endpoint: null
Binding SID = 101
SID List:
[ADJ-5100, 100], 0.4
[ADJ-5103, ADJ-5504], 0.6
5100
5103
5504
5002
5001
Junction Segment B
Headend: B, Color: 100, Endpoint: null
Binding SID = 100
SID List:
[NodeSID-H], 1.0
SR Policy (ingress)
Headend: A, Color: 50 Endpoint: H
SID List:
[ADJ-5002, 100], 0.5
[ADJ-5001, 101], 0.5
Recap SR-MPLS Example

## Slide 4: -02 changes
Changed to informational track
New co-authors
Various text simplification, dropped some unnecessary content
Examples moved to appendix
Manageability considerations
  Liveness - S-BFD behavior
  Monitoring - OAM

## Slide 5: Liveness
General guideline: Run S-BFD on all Junction nodes, on all outgoing segment lists
Required to get full coverage: path to next junction + junction processing
B
C
A
D
G
E
F
H
B
C
A
D
G
E
F
H

## Slide 6: Monitoring
Run Ping/Trace tests originating on all Junction nodes, on all outgoing segment lists
Controller aggregates to produce a full view
Controller/PCE
B
C
A
D
G
E
F
H
38ms
35ms
34ms
37ms
42ms
A->C measures one strand
Controller computes deltas to determine min, max, estimate delay via SID List to C
44ms
43ms
Ping from A to C will be weight hashed out of C unless cycle entropy, which can cascade through multiple junctions

## Slide 7: Next steps
Open to discussions and feedback
OAM SRv6 specific details to explore
Seeking WG adoption