## Slide 1: Multipath Traffic Engineering for Segment Routing
draft-stone-spring-mpte-sr
IETF 123 - Madrid
Andrew Stone (andrew.stone@nokia.com) – Presenter
Vishnu Pavan Beeram – (vbeeram@juniper.net)

## Slide 2: Multipath Traffic Engineering
Introduced in draft-kompella-teas-mpte
Different transport tunnel types concept comprised of:
  Traffic engineered constraints
  ECMP paths
  Non-ECMP Paths – slack x of the shortest path
  Multi-egress nodes and multi-ingress (maybe)
  Unequal weight load balancing per hop
Transport tunnel is represented as a Directed Acyclic Graph (DAG) instead of a Path
Computed by a headend ingress or a PCE
Can be centralized or distributed solution for signaling

## Slide 3: Multipath Traffic Engineering
B
C
A
D
G
E
F
H
20
10
10
10
5
5
5
5
10
10
10
10
B
C
A
D
G
E
F
H
20
10
10
10
5
5
5
5
10
10
10
10
B
C
A
D
G
E
F
H
20
10
10
10
5
5
5
5
10
10
10
10
B
C
A
D
G
E
F
H
20
10
10
10
5
5
5
5
10
10
10
10
Shortest path
Shortest ECMP path
TE Path
Multipath TE DAG
5
Te pruned

## Slide 4: draft-stone-spring-mpte-sr
B
C
A
D
G
E
F
H
Describes a centralized solution to compute and signal a MPTE DAG for SR networks
Uses a Controller/PCE to compute, and PCEP/BGP/Netconf to signal (existing protocols)
The DAG is comprised of Junction Segments deployed on Junction Nodes
  Junction node is a transit node that forwards to one or more interfaces
  Similarity to Replication Segment - except load balanced, not replicated
Junction Segment is comprised of:
  Incoming SID (Binding SID)
  Outgoing SID list(s)
    Next-Junction Segment(BSID) and SR-Path stack
    Weight
A Junction segment is implemented with SR Policy with a single candidate path
Controller/PCE
PCEP/BGP/Netconf

## Slide 5: ….just use SR Policy w/multiple segment lists
Yes !
But… depending on the topological graph and size of the DAG, this could be a significant number of paths.
MSD of the SID stack as you deviate more from shortest path could also be of concern.
Ingress only load balancing vs per junction node load balancing.
Decision to use multiple SID lists or MPTE solution would be topologically dependent.

## Slide 6: Junction Segment Partial, simple example with SR-MPLS
B
C
A
E
F
H
Junction Segment C
Binding SID = 101
SID List:
[5100, 100], 0.4
[5101, 102], 0.6
5100
5101
5201
5301
5501
5002
5001
- Node SIDs are value NodeSID-{letter}
- Link values are adjacency SIDs
- SID List Pos-0 is top of stack
Junction Segment B
Binding SID = 100
SID List:
[NodeSID-H]
Junction Segment F
Binding SID = 102
SID List:
[102], 1.0
Headend-A
SID List:
[5002, 100], 0.5
[5001, 101], 0.5
Could be optimized out like E, used as an example
Takes SR shortest path to H, skips the need for junction on E

## Slide 7: Junction Segment
Junction Segment C – SR Policy
Headend: C
Endpoint: 0.0.0.0
Color: <MID+VERSION>
Binding SID = 101
SID List:
[5100, 101], 0.4
[5101, 102], 0.6
Implemented by SR Policy with a single candidate path
An SR Policy is unique by {Headend, Endpoint, Color}
Multiple endpoints -> use 0.0.0.0
draft-kompella-teas-mpte describes instance of the DAG is the Multipath TED(MPTED), which is identified by the MID and has a version.
  Useful to know DAG membership of the Junction Segment (SR Policy)
  -> encode MID+Version in the color attribute (**)
    Need to make sure color range is reserved block
    ** An idea...perhaps new candidate path property

## Slide 8: Hierarchy
B
C
A
D
G
E
F
H
The ingress SR Policy of the DAG can also have a binding SID
The DAG can be re-used by multiple upstream SR Paths (could be a DAG itself too)
X
Y
Headend-A
BSID-200
Headend-X
SID-List:
[NodeSID-A, 200]
Headend-Y
SID-List:
[NodeSID-A, 200]
DAG 1000

## Slide 9: draft-stone-spring-mpte-sr Other properties
Protocol support (signal/state feedback) – mostly already all there (TBD MID+Version!)
Junction Segment optimization - don’t need on every router - leap-frog transit with use of a SID list
  +ECMP available between Junction segments -> Node SID / Adjacency SID Sets..
Protection
  TI-LFA on each SID list as per usual
    BSID node protection is a more complicated discussion…
Multi-egress -> yes.
Multi-ingress -> kind of… could be managed by controller but unclear how to “request” or describe API input
Broadcast-links -> yes
Optimization – Local/global - DAG MBB:
  Needs more considerations, procedures described and potentially protocol extensions
  Can take the learnings and procedures from SR P2MP Policy

## Slide 10: Informational or Standards track?
New extensions requested or defined -> not yet
Standards track for now, but mainly informational content in document
  May need extensions for things such as signalling MID+Version
  May need extensions to deal with optimization/make before break scenarios
  As MPTE evolves, this document may also need evolve with new/other things

## Slide 11: Next steps
Open to discussions and feedback on this topic
Stay aligned with concepts in draft-kompella-teas-mpte as it evolves
Decide what to do about MID/Version / Color attribute of the Junction Segment if using SR Policy construct
Determine procedure details for optimization/mbb and whether that requires extensions