## Slide 1: Multipath Traffic Engineering for Segment Routing
draft-stone-spring-mpte-sr
IETF 123 - Madrid
Andrew Stone (andrew.stone@nokia.com) – Presenter
Vishnu Pavan Beeram – (vbeeram@juniper.net)

## Slide 2: Multipath Traffic Engineering
Introduced in draft-kompella-teas-mpte
Transport tunnel comprised of:
  Traffic engineered constraints
  ECMP paths
  Non-ECMP Paths – slack x of the shortest path
Transport tunnel is a Directed Acyclic Graph (DAG)
Centralized or distributed compute and signaling
B
C
A
D
G
E
F
H
20
10
10
10
5
5
5
5
10
10
10
10
Multipath TE DAG
Te pruned

## Slide 3: draft-stone-spring-mpte-sr
DAG computed and signaled by controller/PCE
DAG comprised of Junction Nodes
Junction Segment deployed to Junction Nodes
  Incoming SID (Binding SID)
  Outgoing SID list(s)
    SR Path to Junction + Junction SID
    Weight
B
C
A
D
G
E
F
H
Controller/PCE
PCEP/BGP/Netconf

## Slide 4: Junction Segment Partial example with SR-MPLS
B
C
A
E
F
H
Junction Segment C
Binding SID = 101
SID List:
[ADJ-5100, 100], 0.4
[ADJ-5103, ADJ-5504], 0.6
5100
5103
5504
5002
5001
Junction Segment B
Binding SID = 100
SID List:
[NodeSID-H]
SR Policy A
SID List:
[ADJ-5002, 100], 0.5
[ADJ-5001, 101], 0.5

## Slide 5: Junction Segment Realized with SR Policy
Junction Segment C
SR Policy Candidate Path
Headend: C
Endpoint: 0.0.0.0
Color: <MID+VERSION>
Preference 10
Binding SID = 101
SID List:
[ADJ-5100, 100], 0.4
[ADJ-5103, ADJ-5504], 0.6

## Slide 6: Hierarchy
B
C
D
G
E
F
H
X
Y
Headend-A
BSID-200
Headend-XC
SID-List:
[NodeSID-A, 200]
Headend-Y
SID-List:
[NodeSID-A, 200]
DAG 1000
A

## Slide 7: Informational or Standards track?
No new extensions defined yet
Standards track for now until confident do not need any extensions

## Slide 8: Next steps
Open to discussions, feedback and collaboration
Stay aligned with concepts in draft-kompella-teas-mpte
Decide if use of color field acceptable
Determine procedure details for optimization/MBB